## Slide 1: Program Interrupt
A program interrupt refers to the transfer of program control from a currently running program to another service program as a result of an external or internal generated request.
The interrupt has three variations:
  The interrupt is usually initiated by an internal or external signal rather than from execution of an instruction
  The address of the interrupt service program is determined by hardware rather than from the address field of an instruction
  An interrupt procedure usually stores all the information necessary to define the state of the CPU rather than storing only program counter

## Slide 2: Program Interrupt
PSW – collection of all status bit conditions in the CPU
Stored in hardware register and contains the status information that characterizes the state of the CPU, which includes:
  Status bit from last ALU operation
  Specifies the interrupts that are allowed to occur
  Whether the CPU is operating in a supervisor or user mode

## Slide 3: Types of Interrupt
External interrupts: come from input-output devices, from a timing device from a circuit monitoring the power supply, or from any other external source.
  Example: I/O devices requesting transfer of data, I/O devices finished transfer of data, Elapsed time of event , or power failure
  Internal interrupts/Traps arise from illegal or erroneous use of an instruction or data.
    Example: Internal error conditions are register overflow, attempt to divide by zero, an invalid operation code, stack overflow, protection violation

## Slide 4: Types of Interrupt
Software interrupt is initiated by executing an instruction. It is special call instruction that behaves like an interrupt rather than a subroutine call.
It can be used by the programmer to initiate an interrupt procedure at any desired point in the program.

## Slide 5: Microprocessor organization
The design of instruction set for microprocessor is an important aspect of computer architecture
Many computers have instruction set include more than 100 instructions
They also employee various data types and large no. of addressing modes
The factors influencing computer hardware complexity:
  Upgrading existing models
  Adding instruction to translate from high level into machine level
  Developing machines( software to hardware)

## Slide 6: Complex Instruction Set Computer [CISC]
A computer with large no. of instruction
Characteristic features:
  Variable length instruction
  Provide direct manipulation of operands
  Large no. of instruction 100 to 250 provided
  Certain instruction perform specialized tasks
  Variety of addressing modes about 5to 25
  Examples: Digital Equipment Corporation VAX computer and IBM 370 computer

## Slide 7: Reduced Instruction Set Computer [RISC]
Computer that uses fewer instructions with simple construct so they can be executed much faster within the CPU without having to use memory often
Characteristic features:
  Relatively fewer instruction
  Simple addressing modes
  Memory access is limited to load and store instruction
  Large number registers in cpu
  All operations are carried out using register cpu
  Instruction format is fixed
  Instruction are easily decodable
  Instruction executes I single clock cycle
  Control is hardwired
  Few data types in hardware
  Uniform instruction format
  Identical general purpose register
  Compiler support for translation

## Slide 8: Reduced Instruction Set Computer [RISC]
Advantages:
  Instruction is set simplified
  Register manipulation is optimized
  Few addressing mode are simple
  Instruction length is fixed
  Instruction decoding is easy
  Examples: Alpha, ARC, ARM,AVR, MIPS,PA-RISC,PI, POWERPC, SUPERH ,SPARC